## Slide 1: Building Tribrid® files from RAW
Ben Orsburn
Wow. This was a poor format layout choice (sorry)

## Slide 2: In Fusion 3.0 you can build a method FROM a RAW file
BIG SHOUTOUT to Dr. Chris Ashwood who tipped me off to this feature!
How do you do it?
After Fusion Tune 3.0, this button appears

## Slide 3: You may receive error messages. Don’t panic
The changes are likely quite minor

## Slide 4: For Fusion to Lumos method, lower the %RF
Lumos does not require as much RF Lens % to pull in ions

## Slide 5: Lumos has better quadrupole isolation and ETD efficiency
You may obtain better data quality by using a wider isolation window on the Fusion 1 than Fusion 2.
ETD will likely require a higher Max ETD Reagent Injection time on the Fusion 1 than Fusion 2 due to improvements in this hardware on Lumos.